## Slide 1: Sand Island Container Terminal Freight Analysis

## Slide 2: Agenda

## Slide 3: Agenda
Section | Topics
Introduction | Project purpose, data sources and challenges
Methodology | Steps 1-5: Data collection, mapping, processing, calibration
Estimation Models | Two model scenarios
Results & Analysis | Pier proportions, SICT share, top commodities by tonnage
Conclusion | Key takeaways, limitations & considerations

## Slide 4: Introduction

## Slide 5: Project Purpose
Estimate types and volumes of freight commodities arriving at Sand Island Container Terminal (SICT) via water for 2024
Support transportation planning and infrastructure assessment for the Sand Island corridor
Identify all inbound cargo at SICT piers that must exit via the Sand Island Access Road bridge
Directly applicable to bridge traffic analysis

## Slide 6: Data Sources
Source | Description | Use in Analysis
FAF 5.7.1 Regional | USDOT freight flow data by commodity | Commodity volumes & distributions
Honolulu Harbor 2050 Master Plan | HDOT pier capacity data | Pier-specific allocations
SICT Wharfage Data | Actual port throughput (FY2025) | Calibration of FAF estimates
Key Temporal Assumptions:
FAF reference year: Calendar year 2024 estimates
SICT wharfage period: July 2024 - June 2025 (FY2025)
Assumption: One-year wharfage data is representative of CY2024 volumes

## Slide 7: Data Challenges
No SICT-specific data: No publicly available dataset with detailed commodity breakdown for SICT
Regional FAF data: Freight Analysis Framework (FAF) covers "Honolulu HI" region, not individual piers
Disaggregation needed: Multiple sources used to estimate SICT's share of regional flows
Limited actual data: SICT wharfage data provides totals but lacks commodity detail
Capacity as proxy for flow: No actual commodity-by-pier data exists; pier capacity proportions from the Master Plan are used as a proxy for actual throughput distribution

## Slide 8: Methodology

## Slide 9: Methodology Overview
Step | Input | Output
1. Pier Operations Data | Honolulu Harbor 2050 Master Plan | Capacity proportions per pier
2. Cargo Type Definitions | Master Plan categories | 5 types: Container, RO/RO, Break-Bulk, Liquid-Bulk, Dry-Bulk
3. Commodity Mapping | 42 FAF commodity codes (SCTG2) | Cargo type + containerization % per commodity
4. Data Processing & Pier Distribution | FAF 5.7.1 + Steps 1–3 | Filter → Aggregate → Distribute to piers
5. SICT Calibration | Actual port wharfage data | Scale FAF to match actuals → 2 output scenarios

## Slide 10: Step 1: Pier Operations Data Collection
Source: Honolulu Harbor 2050 Master Plan (manual extraction)
Output: Pier Operations and Cargo Inventory spreadsheet
Data Extracted | Description
Pier identification | All piers in Honolulu Harbor
Container capacity (TEUs) | Annual container handling capacity
RO/RO capacity | Annual vehicle handling capacity
Break-Bulk capacity (Tons) | Annual break-bulk capacity
Liquid-Bulk capacity (Bbls) | Annual liquid-bulk capacity
Dry-Bulk capacity (Tons) | Annual dry-bulk capacity
Derived: Pier proportions = Pier Capacity / Total Harbor Capacity

## Slide 11: Step 2: Cargo Type Definitions
Five cargo type categories defined from the Master Plan:
Cargo Type | Description
Containers | Standardized shipping containers (TEUs)
RO/RO | Roll-on/Roll-off vehicles and wheeled cargo
Break-Bulk | Non-containerized general cargo
Liquid-Bulk | Petroleum products, chemicals, liquids
Dry-Bulk | Coal, aggregates, grain, dry commodities

## Slide 12: Step 3: Commodity Mapping (FAF SCTG2 Codes to Cargo Types)
Source: Commodity Dictionary spreadsheet
Mapped all 42 FAF commodity codes (SCTG2) to cargo types
Assigned containerization proportions for each commodity
Handling Type | Container % | Example Commodities
Fully Containerized | 100% | Manufactured goods, perishables
Fully Non-Containerized | 0% | Grains, aggregates, petroleum
Mixed-Mode | 10-90% | Milled grains (90% container, 10% bulk)

## Slide 13: Step 4: Data Processing & Pier Distribution
FAF data is filtered for Honolulu water-based inbound freight
Filtering Logic:
Flow Type | Origin | Destination | Mode Filter
Domestic Water | Other U.S. (not Honolulu) | Honolulu HI | dms_mode = Water
Import Direct | Foreign → Honolulu | Honolulu HI | fr_inmode = Water
Import Transshipped | Foreign → Other U.S. → Honolulu | Honolulu HI | dms_mode = Water
Processing Pipeline:
1. Filter FAF for Honolulu water-based inbound freight (above logic)
2. Aggregate filtered data by FAF commodity (SCTG2) (sum tonnage)
3. Merge cargo type assignments from Commodity Dictionary (Step 3)
4. Distribute commodity totals to piers based on capacity proportions

## Slide 14: Step 4 (cont.): Distribution Logic
Three handling scenarios based on containerization proportion:
Scenario | Container % | Distribution Method
Fully Containerized | 100% | All tonnage distributed by Container pier proportions
Fully Non-Containerized | 0% | All tonnage distributed by Bulk/Break-Bulk/RO-RO pier proportions
Mixed-Mode | 1-99% | Split: containerized share → Container proportions; remainder → Alternative type proportions
Example: Meat/seafood (10,000 tons, 95% containerized, Alternative = Break-Bulk)
9,500 tons (95%) → distributed to piers by their Container proportions
500 tons (5%) → distributed to piers by their Break-Bulk proportions

## Slide 15: Step 5: SICT Calibration
FAF model estimated ~132,000 tons for SICT piers
Actual port data showed ~4,084,000 tons inbound
Solution: Scale FAF data to match actual throughput while preserving commodity proportions
Source | Total Tons | Notes
FAF Model | ~132,000 | SICT receives 0% allocation for Liquid-Bulk and Dry-Bulk per pier capacity proportions
Actual Port Data | 4,084,234 | Actual wharfage throughput

## Slide 16: Step 5 (cont.): Classification Rules
FAF commodities are mapped to SICT wharfage categories using two dimensions:
Dimension | Rule
SICT-Type = "Vehicles" | FAF commodities (SCTG2): "Motorized vehicles" and "Transport equip."
SICT-Type = "Cargo Non Vehicles" | All other FAF commodities (SCTG2)
Containerized = Yes | When cargo_type = "Containers"
Containerized = No | When cargo_type ≠ "Containers" (Break-Bulk, RO/RO, Dry-Bulk)

## Slide 17: Step 5 (cont.): Scaling to Actual Port Data
Actual Port Data Breakdown (Scaling Targets):
SICT-Type | Containerized | Actual Port Tons
Cargo | Yes | 3,958,177
Cargo | No | 8,130
Vehicles | Yes | 27,184
Vehicles | No | 90,742
Scaling Formula — For each (SICT-Type, Containerized) group:
tonnage_scale = Actual Port Tons / FAF Model Tons
scaled_tons = FAF_tons × tonnage_scale
Preserves relative commodity proportions within each group

## Slide 18: Estimation Models

## Slide 19: Two Model Scenarios
Model | Description
Model 1: FAF Baseline | Original FAF estimates for SICT
Model 2: Calibrated to Actuals | FAF estimates scaled to actual port tonnage
Note: Although SICT does receive jet fuel, Liquid-Bulk cargo is excluded from our estimation models. For modeling purposes, SICT is assumed to handle only Containers, RO/RO, and Break-Bulk cargo. Liquid-Bulk operations (petroleum products, chemicals) are primarily handled at other Sand Island facilities and Pier 30, and are typically transported via pipeline rather than by truck over the bridge.

## Slide 20: Results

## Slide 21: Pier Capacity Proportions
Honolulu Harbor pier capacity allocation by cargo type:
Pier | Container | RO/RO | Break-Bulk | Liquid-Bulk | Dry-Bulk
1 (1A, 1B) | 5% | 24% | 16% | 0% | 0%
2 (2A, 2B, 2C) | 0% | 1% | 0% | 0% | 0%
19 & 20 | 0% | 10% | 0% | 0% | 0%
29 | 5% | 1% | 18% | 0% | 0%
30 | 0% | 0% | 0% | 100% | 0%
31, 32, 33 | 0% | 44% | 0% | 0% | 0%
34 | 0% | 1% | 0% | 0% | 0%
39 & 40 | 13% | 8% | 56% | 0% | 0%
51, 52, 53 (SICT) | 77% | 13% | 10% | 0% | 0%
60 | 0% | 0% | 0% | 0% | 100%
Key Insight: SICT dominates container handling (77%).

## Slide 22: SICT Share of Honolulu Harbor (FAF Model)
Overall SICT Share (scoped to SICT cargo types: Containers, RO/RO, Break-Bulk):
SICT handles Containers, RO/RO (automobiles), and Break-Bulk cargo. The share calculation is scoped to these three cargo types for a like-for-like comparison.
Metric | SICT | Honolulu Total | SICT Share
Tonnage | 132,035 tons | 214,437 tons | 61.6%

## Slide 23: Top Commodities: FAF Model (by Tonnage)
Commodity | Tons | % of SICT
Nonmetal min. prods. | 16,887 | 12.8%
Mixed freight | 15,704 | 11.9%
Paper articles | 12,458 | 9.4%
Articles-base metal | 10,205 | 7.7%
Milled grain prods. | 9,441 | 7.2%

## Slide 24: Top Commodities: Scaled Model (by Tonnage)
Key Insight: After calibration to actual port throughput (~4.1M tons vs. ~132K FAF estimate), the top commodities remain consistent with the FAF baseline. Construction materials, mixed freight, and processed goods dominate SICT — these are the goods most likely transported by truck over the Sand Island Access Road bridge.
Commodity | Scaled Tons | % of SICT
Nonmetal min. prods. | 537,225 | 13.2%
Mixed freight | 499,603 | 12.2%
Paper articles | 394,087 | 9.6%
Articles-base metal | 316,099 | 7.7%
Milled grain prods. | 300,350 | 7.4%

## Slide 25: Conclusion

## Slide 26: Key Takeaways
Combined FAF regional data with actual port data for robust estimates
Preserved FAF commodity detail while matching observed throughput
Produced pier-level allocations based on operational capacity
SICT handles 61.6% of Honolulu Harbor's tonnage (scoped to Containers, RO/RO, and Break-Bulk)
Construction materials, mixed freight, and processed goods dominate SICT — directly relevant to bridge truck traffic

## Slide 27: Limitations & Considerations
Limitation | Impact | Mitigation
FAF underestimates SICT throughput (~132K vs ~4.1M tons) | Scaling factors are large | Calibrated with actual wharfage data
Temporal mismatch: FAF CY2024 vs. wharfage FY2025 | Minor seasonal variation possible | One full year assumed representative
Pier capacity proportions used as a proxy for actual throughput distribution | Actual utilization may differ from designed capacity | Best available approach given data constraints